## Slide 1: 6809 interface timing
1,1
1,0
BA
BS
RW
D0
D1
D2
D7
Q
D0
D1
D7
E
0,0
6809 write data
D7
0,0
Q is high for 40 clock cycles and low for 20 clocks – 60 total @ 20MHZ = 333.3 kHz
E trails Q by 8 clock cycles
Write data from the 6809 isn’t available until E goes high
For a read cycle the full 16 bit address must be read first before data can be supplied
A14
A15
D6
BSY
LIC
AVMA
SW1
SW2

## Slide 2: 6809 interface
6809E
299
299
299
299
D0-7
A0-7
A8-15
BA
BS
R/W
BUSY
LIC
AVMA
S0,S1
IRQ
RESET
RESET
164
E
Q
Q
CLK
Q
S0,S1
Q CLK
D
IRQ
R/W
G
+

## Slide 3: 6809 interface
Description:
CLK is a free running 6 to 40 MHz clock generated by the FPGA. The CLK signal must be at least 6MHz to meet the minimum clock frequency of the 6809E. The FPGA also generates a reference Q clock signal for the 6809E. CLK is fed into a 74HCT164 shift register to generate the E clock by delaying Q by 8 clock cycles. The E clock is used to synchronize data transfer. A mirror image of the E clock is generated internally to the FPGA.
The leading edge of E causes 32 bits of data to be loaded into the shift register. The shift registers can’t be loaded until the E clock edge because that’s when the write data becomes available from the 6809E. Data is transferred to or from the FPGA while the E clock is high. Note that the data for a 6809E read cycle must be valid a setup time (80 ns) before the falling edge of the E clock. Hence the high time of 40 clocks to allow time to transfer 32 bits plus a couple of cycles of setup time.
After 24 bits are shifted, it can be determined whether the 6809E is performing a read or write cycle. If the 6809E is performing a read cycle, the data is fetched from memory, then shifted back into a 74HCT299 shift register.
If the cycle is a read cycle, the R/W signal of the 6809E enables the output from the 74HCT299 shift register onto the data bus.